# Hey Emacs, this is a -*- makefile -*-

# AVR-GCC Makefile template, derived from the WinAVR template (which

# is public domain), believed to be neutral to any flavor of "make"

# (GNU make, BSD make, SysV make)

MCU = atmega328p

F_CPU=16000000

FORMAT = ihex

TARGET = main

SRC = $(TARGET).c

ASRC =

OPT = s

# Name of this Makefile (used for "make depend").

MAKEFILE = Makefile

# Compiler flag to set the C Standard level.

# c89 - "ANSI" C

# gnu89 - c89 plus GCC extensions

# c99 - ISO C99 standard (not yet fully implemented)

# gnu99 - c99 plus GCC extensions

CSTANDARD = -std=gnu99

#CSTANDARD = -std=gnu11

# Place -D or -U options here

CDEFS =

# Place -I options here

CINCS =

CDEBUG = -g

CWARN = -Wall -Wstrict-prototypes

CTUNING = -funsigned-char -funsigned-bitfields -fpack-struct -fshort-enums

CFLAGS = $(CDEBUG) $(CDEFS) $(CINCS) -O$(OPT) -O2 $(CWARN) $(CSTANDARD) $(CEXTRA)

CPPFLAGS=-DF_CPU=$(F_CPU)L

ASFLAGS = -Wa,-adhlns=$(<:.S=.lst),-gstabs

#Additional libraries.

# Minimalistic printf version

PRINTF_LIB_MIN = -Wl,-u,vfprintf -lprintf_min

# Floating point printf version (requires MATH_LIB = -lm below)

PRINTF_LIB_FLOAT = -Wl,-u,vfprintf -lprintf_flt

PRINTF_LIB =

# Minimalistic scanf version

SCANF_LIB_MIN = -Wl,-u,vfscanf -lscanf_min

# Floating point + %[ scanf version (requires MATH_LIB = -lm below)

SCANF_LIB_FLOAT = -Wl,-u,vfscanf -lscanf_flt

SCANF_LIB =

MATH_LIB = -lm

LDFLAGS = $(EXTMEMOPTS) $(LDMAP) $(PRINTF_LIB) $(SCANF_LIB) $(MATH_LIB)

# Programming support using avrdude. Settings and variables.

AVRDUDE_PROGRAMMER = arduino

AVRDUDE_PORT = /dev/ttyACM0

AVRDUDE_BUDRATE = 115200

AVRDUDE_WRITE_FLASH = -U flash:w:$(TARGET).hex

AVRDUDE_WRITE_EEPROM = -U eeprom:w:$(TARGET).eep

AVRDUDE_BASIC = -p $(MCU) -P $(AVRDUDE_PORT) -c $(AVRDUDE_PROGRAMMER) -b $(AVRDUDE_BUDRATE)

AVRDUDE_FLAGS = $(AVRDUDE_BASIC) $(AVRDUDE_NO_VERIFY) $(AVRDUDE_VERBOSE) $(AVRDUDE_ERASE_COUNTER)

CC = avr-gcc

OBJCOPY = avr-objcopy

OBJDUMP = avr-objdump

SIZE = avr-size

NM = avr-nm

AVRDUDE = avrdude

REMOVE = rm -f

MV = mv -f

# Define all object files.

OBJ = $(SRC:.c=.o) $(ASRC:.S=.o)

# Define all listing files.

LST = $(ASRC:.S=.lst) $(SRC:.c=.lst)

# Combine all necessary flags and optional flags.

# Add target processor to flags.

ALL_CFLAGS = -mmcu=$(MCU) -I. $(CFLAGS) $(CPPFLAGS)

ALL_ASFLAGS = -mmcu=$(MCU) -I. -x assembler-with-cpp $(ASFLAGS)

# Default target.

all: build

build: elf hex eep program

elf: $(TARGET).elf

hex: $(TARGET).hex

eep: $(TARGET).eep

lss: $(TARGET).lss

sym: $(TARGET).sym

.SUFFIXES: .elf .hex .eep .lss .sym

.elf.hex:

$(OBJCOPY) -O $(FORMAT) -R .eeprom $< $@

.elf.eep:

-$(OBJCOPY) -j .eeprom --set-section-flags=.eeprom="alloc,load" \

--change-section-lma .eeprom=0 -O $(FORMAT) $< $@

# Create extended listing file from ELF output file.

.elf.lss:

$(OBJDUMP) -h -S $< > $@

# Create a symbol table from ELF output file.

.elf.sym:

$(NM) -n $< > $@

# Link: create ELF output file from object files.

$(TARGET).elf: $(OBJ)

$(CC) $(ALL_CFLAGS) $(OBJ) --output $@ $(LDFLAGS)

# Compile: create object files from C source files.

.c.o:

$(CC) -c $(ALL_CFLAGS) $< -o $@

# Compile: create assembler files from C source files.

.c.s:

$(CC) -S $(ALL_CFLAGS) $< -o $@

# Assemble: create object files from assembler source files.

.S.o:

$(CC) -c $(ALL_ASFLAGS) $< -o $@

# Program the device.

program: $(TARGET).hex $(TARGET).eep

$(AVRDUDE) $(AVRDUDE_FLAGS) $(AVRDUDE_WRITE_FLASH) $(AVRDUDE_WRITE_EEPROM)

# Target: clean project.

clean:

$(REMOVE) $(TARGET).hex $(TARGET).eep $(TARGET).cof $(TARGET).elf \

$(TARGET).map $(TARGET).sym $(TARGET).lss \

$(OBJ) $(LST) $(SRC:.c=.s) $(SRC:.c=.d)

depend:

if grep '^# DO NOT DELETE' $(MAKEFILE) >/dev/null; \

then \

sed -e '/^# DO NOT DELETE/,$$d' $(MAKEFILE) > \

$(MAKEFILE).$$$$ && \

$(MV) $(MAKEFILE).$$$$ $(MAKEFILE); \

fi

echo '# DO NOT DELETE THIS LINE -- make depend depends on it.' \

>> $(MAKEFILE); \

$(CC) -M -mmcu=$(MCU) $(CDEFS) $(CINCS) $(SRC) $(ASRC) >> $(MAKEFILE)

.PHONY: all build elf hex eep lss sym program coff extcoff clean depend